## Slide 1: Time Series Forecasting
Argentina Oil and Gas Production Prediction
using SARIMAX model
Source Data: Secretaría de Energía de la Nación Argentina

## Slide 2: Time series has a difficult forecasting approach but not impossible
We are going to use Source Data from Argentina Oil and Gas Production
Period: Jan-2009 to Jul-2022

## Slide 3: Time Series Models
Auto Regressive (AR)
Moving Average (MA)
Auto Regressive Moving Average (ARMA)
Auto Regressive Integrated Moving Average (ARIMA)
Seasoned Auto Regressive Integrated Moving Average (SARIMA)
Seasoned Auto Regressive Integrated Moving Average with Exogenous Factors (SARIMAX)

## Slide 4: Auto Regressive Models
Representation of a type of random process
Specifies that the output variable depends linearly on its own previous values and on a stochastic term
The model is in the form of a stochastic difference equation
The notation AR(p) indicates an autoregressive model of order p. The AR(p) model is defined as:
where are the parameters of the model and is white noise

## Slide 5: Moving Average Models
Model univariate time series
Specifies that the output variable is Cross-Correlated with a non-identical to itself random-variable
The notation MA(q) indicates a moving average model of order p:
where are the parameters of the model and is white noise
Conceptually is a linear regression of the current value of the series against current and previous white noise error terms

## Slide 6: Auto Regressive Moving Average (ARMA)
Describes (weakly) stationary stochastic process
Combination of AR and MA models
The notation ARMA(p, q) indicates a model with p autoregressive terms and q moving-average terms:
Where are the parameters of the model and is white noise

## Slide 7: Auto Regressive Integrated Moving Average (ARIMA)
Combination of AR and MA models
Applied when data show evidence of non-stationary where an initial differencing step can be applied one or more times to eliminate the non-stationary of the mean function, aka trend. These is the ‘I’ Part
The notation ARIMA(p, d, q) indicates a model with p autoregressive terms, d degrees of differencing and q moving-average terms

## Slide 8: Seasoned Auto Regressive Integrated Moving Average (SARIMA)
Same as ARIMA with seasonal component
The notation SARIMA(p, d, q) x (P, D, Q) indicates a model with p autoregressive terms, d degrees of differencing and q moving-average terms and the uppercase PDQ refers to the autoregressive, differencing and moving average terms of the seasonal part
Seasoned Auto Regressive Integrated Moving Average with exogenous factors (SARIMAX)
Same as SARIMA but updated.
Can deal with external effects

## Slide 9: Production Time Series
 | TotalPet(m3/d) | TotalGas(km3/d)
count | 163 | 163
mean | 84443.91 | 123918.35
std | 6495.75 | 7495.47
min | 71163.54 | 105860.82
25% | 79468.45 | 117651.24
50% | 84406.51 | 123464.28
75% | 88486.06 | 128298.84
max | 100044.07 | 144420.97

## Slide 10: Production Time Series 12-month Rolling Mean

## Slide 11: Production Time Series Seasonal Decompose

## Slide 12: Checking Stationary Data Series
Dick-Fuller Statistical Test
Data is not stationary -- > Null Hypothesis (H0)
If p-value < 0.05 then H0 is rejected
For Oil Production
p-value = 0.1692  H0 is not rejected
Differencing one month, p-value = 1.292e-18 < 0.05 --> Stationary Data
For Gas Production
p-value = 9.94e-24 < 0.05 --> Stationary Data
No differencing calculation needed

## Slide 13: ACF and PCF Visualization
Oil
Gas

## Slide 14: Training Models
Train Set: Jan-2009 to Jan-2022 Test Set: Jan-2022 to Jul-2022
Last 7 months
4,5 % of Data is used to test

## Slide 15: Models Results
Oil
Model: ((2, 1, 0), (2, 2, 1, 12))
Min AIC: 1929.07
 | coef | std err | z | P>¦z¦ | [0.025 | 0.975]
ma.L1 | 0.1214 | 0.241 | 0.504 | 0.614 | -0.350 | 0.593
ma.L2 | 0.0274 | 0.252 | 0.109 | 0.913 | -0.466 | 0.520
ar.S.L12 | -0.3687 | 0.307 | -1.201 | 0.230 | -0.971 | 0.233
ma.S.L12 | -0.6111 | 0.235 | -2.595 | 0.009 | -1.073 | -0.150
ma.S.L24 | 0.1505 | 0.177 | 0.852 | 0.394 | -0.196 | 0.497
sigma2 | 3.143e+08 | 3.5e-10 | 8.97e+17 | 0.000 | 3.14e+08 | 3.14e+08
Gas
Model: ((0, 0, 2), (1, 2, 2, 12))
Min AIC: 2287.58
 | coef | std err | z | P>¦z¦ | [0.025 | 0.975]
ar.L1 | -0.1022 | 0.095 | -1.081 | 0.280 | -0.287 | 0.083
ar.L2 | -0.0307 | 0.084 | -0.364 | 0.716 | -0.196 | 0.135
ar.S.L12 | -0.2662 | 0.167 | -1.597 | 0.110 | -0.593 | 0.061
ar.S.L24 | -0.2186 | 0.090 | -2.438 | 0.015 | -0.394 | -0.043
ma.S.L12 | -1.1773 | 0.246 | -4.786 | 0.000 | -1.659 | -0.695
ma.S.L24 | 0.1468 | 0.177 | 0.831 | 0.406 | -0.199 | 0.493
sigma2 | 3.912e+06 | 1.05e-07 | 3.72e+13 | 0.000 | 3.91e+06 | 3.91e+06

## Slide 16: Gas Model Diagnostic Plots

## Slide 17: Oil Model Diagnostic Plots

## Slide 18: Models Residuals Plot
Less residual variance in Oil than Gas

## Slide 19: Models ACF and PACF Visualization
Oil
Gas

## Slide 20: Models Predictions
As we move forward in predicted time, confidence intervals start to diverge

## Slide 21: What happens if we change Data Units?

## Slide 22: Models Predictions
Gas in Mm3/d and Oil in km3/d, as we can see Forecasting changes

## Slide 23: Models Summary
Data | SARIMAX Model | AIC | RMSE | % RMSE / mean
Total Gas (km3/d) | ((0, 0, 2), (1, 2, 2, 12)) | 2287 | 16645 | 13,43
Total Gas (Mm3/d) | ((0, 2, 2), (0, 2, 2, 12)) | 773 | 9.79 | 7.90
Total Pet (m3/d) | ((2, 1, 0), (2, 2, 1, 12)) | 1929 | 1047.88 | 1.24
Total Pet (km3/d) | ((2, 1, 2), (2, 1, 2, 12)) | 463 | 1.15 | 1.35